## Slide 1: LinkComm v3 – “Common Communicator”
LinkComm can connect to SatLink 3 via WiFi to view live readings, view logged readings, view diagnostics/status, calibrate, and setup.

## Slide 2: LinkComm v3 – “Common Communicator”
Multi-logger
  SatLink3, Xlink, Xpert, 8310
Multi-platform
  Windows, Mac, iOS, Android
Serial & TCP/IP
  WiFi
  Redirector
Multi-screen
  Desktop, tablet, phone
Touch enabled
Enhanced experience
  Graphing, pics, animations
  High performance
Single source

## Slide 3: LinkComm v3 – Station Management
First screen you see
Remembers station definitions
  Automatic saves
Station type
Connection Settings
  Serial Port (incl. USB serial)
  Station WiFi
  Redirector
  TCP/IP
Enhanced setup data
  Site notes
  Site pictures
Browse for pics, or use device camera
Scroll to see more (vertical)

## Slide 4: LinkComm v3 – Dashboard Tab
First screen after “Connect”
View station’s current state
  Current status
  Current measurement values
  Graphs of recent values (1 week)
Sync button in header
  Setup in sync and recording ON
  Setup has changed
  Recording is OFF
Connect button in header
Buttons to “Refresh Status”, “Clear Data”, and “Show Details”

## Slide 5: LinkComm v3 – Measurements Tab
First screen after “Work Offline”
Define configuration and meta data for each measurement
Select measurement in left pane
Sensor templates
  Default configuration
  Sensor image
  Wiring diagram
Custom sensor image
Custom wiring diagram
Send setup after making changes!

## Slide 6: LinkComm v3 – Data Tab
Zoom-in by click-and drag
Zoom-out by double-tap/click
Check to show/hide data sets
Right-click (or touch) graph for menu options to
  Select/deselect all series
  Show points
Shows recent data by default
Save download to file
Save graph to file
Share to DropBox

## Slide 7: LinkComm v3 – Telemetry Tab
Telemetry Configuration
  Transmission schedule and setup
  Internet, Listening, SMS
  Modem settings, etc.
Telemetry status
Test operations
  Tx Now
  Message Check
  Show Tx Data
Other Setup
  WiFi Settings
  Modbus Settings

## Slide 8: LinkComm v3 – Diagnostics Tab
Firmware Versions
Firmware Diagnostics
  Recent asserts and exceptions
LinkComm data usage
LinkComm version
Options to
  Save file to share with customer service
  Terminal dialog (send commands)
  Data Flow dialog (view data in hex)
  SDI-12 dialog to send SDI-12 commands to sensors attached to station
  Set Clock, Factory Defaults, Reboot