## Slide 1: High resolution dynamics of HABs in two Cape Cod ponds
Jeff Hollister, Stephen Shivers, Betty Kreakie, Don Cobb, Sophie Fournier, Laura Erban, Tara Burke

## Slide 2: Where, When
  Shubael Pond and Hamblin Pond
    Compliments SDR d
    A-pod deployment?
  June to November
    Started 2021

## Slide 3: Why High Resolution?
  Why High Resolution?
    We know the general process (nutrients and temperature)
    Don’t know fine scale triggers

## Slide 4: Why High Resolution?
  Why High Resolution?
    Forecasting requires high resolution
      Butitta et al 2017 (3500 points in 2.5 ha/6 acre lake)
      Ortiz el al. 2020 (every 15 minutes)
      Wilkinson et al. 2018 (every 5 minutes)
      Dakos et al. 2012 (1000's of equal time steps)

## Slide 5: How: HABS over space
  Fast Limnological Automated Measurments (FLAMe)
    University of Wisconsin Center for Limnology: https://flame.wisc.edu
    On-board flow through system
    Multiparameter Sonde
    Optical nitrate sensor
    Measurements approx. every 20 meters
    Twice a month
    Work in progress!

## Slide 7: How: HABS over time
  Nexsens CB-150 Buoy
    Multiparameter sonde
      Temperature, dissolved oxygen, pH, conductivity, tubirdity, FDOM, chlorophyll, phycocyanin
    Optical nitrate sensor
    Weather station
  FieldKit Water with solar
    Temperature, dissolved oxygen, pH, conductivity
  Fixed location
  Every 15 minutes

## Slide 8: Preliminary Results
  Shhhh

## Slide 9: Questions: Happy Field Crew